## Slide 1: SN Tool Introduce
2013/07/17
Presenter (Wenping Liu)
Department (ACS7/ST)

## Slide 2: Agenda
SN write option introduce
  Barcode、IMEI、BT Address、Wi-Fi Mac Address
  Hdcp & Drm key
  SN Tool special setting
New SN Tool UI
  SN Tool new main panel
  New UI Modify Item
    Add Login Identify : Engineer & Operator
    System config
    Move some select option to menu
    New scan data dialog
SN Tool write procedure example
  Barcode & IMEI(Meta Mode)
  Barcode / IMEI / BT / Wi-Fi (Meta Mode)
  Hdcp & Drm key(Meta Mode)
How to debug when write fail

## Slide 3: SN write option introduce

## Slide 4: Barcode、IMEI、BT Address 、Wi-Fi Mac Address
Barcode
  Production Serial Number for a PCBA, is usually use to identify PCBA. Each
  PCBA should have a barcode number to keep the its test item in production line.
  Barcode should be write to PCBA after download and before ATE calibration,
  because in the calibration station, ATE Tool will write Calibration flag and NSFT
  flag to barcode. If you rewrite use SN Tool, these flags will be cover.
  Support max 64 characters, composed of letters and numbers.
IMEI
  International Mobile Equipment Identity, is a number unique to every GSM and WCDMA phone.
  Must be 15 decimal digits, 14 decimal digits + 1 checksum digit.
BT Address
  Must be 12 characters, composed of letters(a - f or A - F) and numbers.
Wi-Fi Mac Address
  Must be 12 characters, composed of letters(a - f or A - F) and numbers.

## Slide 5: Hdcp & Drm key
Hdcp key
  High-bandwidth Digital Content Protection, when users of illegal copying, the technology will be interference, reduce duplicated image quality, so as to protect the content.
  the hdcp key bin need purchased by customer.
  Write hdcp key need Ap database.
Drm key
  Some Digitized audio programs have Protection of digital programs authorized centers, so must have drm key when Broadcast program
  Write drm key don`t need any database

## Slide 6: Special setting
SN Tool Menu - Option
  Mode select
    META mode
      Target will enter META mode to write Barcode、IMEI、BT、Wi-Fi
      Need select correct database file
      Support all Feature Phone、Smart Phone and Datacard product
    AT mode
      Target will normal bootup and use AT cmd to write Barcode、IMEI、BT、 Wi-Fi
      Don`t need select database file
      Current only support feature phone to write barcode、IMEI
  FeaturePhone Option / AT_SDS
    Use AT mode and want to trigger backup data to SDS, need select this option
  Datacard
    For Datacard product, enable USBSwitchTool
  External Modem
    For DualTalk project, enable preloader comPort switch to single comPort
  SP Security USB
    For Smart Phone security chip

## Slide 7: Special setting
  SN Tool Menu - BT&IMEI
  Check Sum
    Enable IMEI checksum mechanism, the last IMEI bit will be calculate and replace
    last bit get from UI. Ex, UI input ‘1111 1111 1111 111’ will be replace by
    ‘1111 1111 1111 119 ’, the ‘9’ is the checksum bit.
  Lock IMEI
    if check the Lock IMEI, this mean the IMEI can only write one time when current operator is successfully. If you want to rewrite IMEI again, you must Format FAT!!!
If is MT6582 smart phone, modify SN_SETUP.txt in installation directory
  Is MT6582 World Phone
    True: for MT6582 smart phone
    False: for another without world phone feature platform, include feature phone
  World Phone MD Index
    1: Enable Modem1 when boot up
    2: Enable Modem2 when boot up
  World Phone SW Version
    3 : WCDMA phone
    5 : TDD phone

## Slide 8: New SN Tool UI

## Slide 9: SN Tool new main panel
Old SN Tool
New SN Tool

## Slide 10: New UI Modify Item
Add menu – “Identify”
  Engineer : Login in engineer mode
    Can Modify UI configuration
    Switch To operator don`t need password
  Operator : Login in operator mode
    No authority modify UI configuration
    Switch to engineer mode need password
Add button – “System Config”
  Setup write barcode、IMEI、BT、Wi-Fi option
  Setup the database files
Move some select option to menu
  AT or Meta mode select  ‘ Option’
  Hdcp、DRMKey file select  ‘ Hdcp&Drmkey’
  Datacard、External Modem、SP Security USB  ‘Option’

## Slide 11: Engineer Mode
Engineer Mode
  Engineer mode use for setup all write option, such as select database file, setup
  head check string. The mode is the default login mode, The default password is ‘0000’.
  Use the Menu – ’Identity->Engineer->SwitchToOperator’ to switch to operator
  mode, don`t password.
  Use the Menu – ’Identity-> Engineer-> ChangePasswd’ to modify the engineer password.

## Slide 12: Operator Mode
  Operator Mode
  Operator mode have no authority
  modify UI configuration.
  This mode only have select comPort
  num、click Quit and Start button authority.
  ‘Identify->Operator->SwitchToEngineer’
  Switch to engineer mode, need input the
  correct engineer password.

## Slide 13: System config
Function Select
  The option is about which type data
  will be write to target at one time. Ex,
  if select IMEI&BT, you can write IMEI
  and BT address to target at one time.
  Header Option
  For you want to check the scan data
  is valid or not, turn on the header check.
  Ex, if barcode previous 4bits must “1234”,
  turn on check barcode header, and
  configuration the barcode header string
  is “1234”.
  IMEI Option
  IMEI special option
  Data Base
  Select database files

## Slide 14: New scan data dialog
Scan Data
  Enable the edit control option base on
  what do you select in the configuration panel.
  If Header check is turn on, the corresponding
  header string will show on edit control tail.
  The current scan data will be highlight.
  The edit control don`t need scan again when
  scan data finish and header check pass.
  When finish scan all data and click ‘OK’,
  tool will check all data is valid or not. If the
  data is invalid, corresponding edit control
  will be highlight.
  When finish one write flow, this panel
  will be show again.

## Slide 15: SN Tool write procedure example

## Slide 16: Barcode & IMEI(Meta Mode)
1、select comPort – UART or USB VCOM
2、select target type – FP/SP/Rndis Dongle/…
3、select write mode – MEAT mode /AT mode
4、click ‘System Config’ button
5、Function select – choose Barcode & IMEI
6、Header option – if check data, turn it on
7、select correct database files
8、Click ‘Start’ to scan data
9、Insert cable make phone enter ‘META mode’
10、If Write Result Indicator turn
- Green mean write success
- Red mead write fail
5
6
8
3
10
4
2
1
9
Enter
Meta
mode

## Slide 17: Barcode / IMEI / BT / Wi-Fi(Meta Mode)
1、select comPort – UART or USB VCOM
2、select target type – FP/SP/Rndis Dongle/…
3、select write mode – MEAT mode /AT mode
4、click ‘System Config’ button
5、Function select – choose Barc/IMEI/BT/Wi-Fi
6、Header option – if check data, turn it on
7、select correct database files
8、Click ‘Start’ to scan data
9、Insert cable make phone enter ‘META mode’
10、If Write Result Indicator turn
- Green mean write success
- Red mead write fail
5
6
8
3
10
4
2
1
9
Phone
Enter
Meta
mode

## Slide 18: IMEI / BT(Meta Mode)
1、选择 端口类型 – UART 或者 USB VCOM
2、选择 手机类型 – FP/SP/Rndis Dongle/…
3、选择 写号模式 – MEAT mode /AT mode
4、点击‘系统配置’ 按钮
5、写号类型选项 – 选择写 IMEI & BT
6、头部检测功能选项 – 需要检测数据正确性, 勾选‘On/Off’按钮
7、选择正确的Database文件
8、点击’开始’按钮输入或扫描正确的数据
9、插入USB或UART数据线，让手机进入META模式
10、如果写操作结果指示器变成
- 绿色表示写操作成功
- 红色表示写操作失败
5
6
8
3
10
4
2
1
9
手机开机进META 模式

## Slide 19: Hdcp & Drm key(Meta Mode)
1、select comPort – UART or USB VCOM
2、select target type – FP/SP/Rndis Dongle/…
3、select write HDCP & DRM Key Install
4、select Hdcp Bin File & DRMKey File
5、click ‘System Config’ button
6、select correct AP database file for write Hdcp
7、Click ‘Start’ to write data
8、Insert UART/USB cable make phone enter ‘META mode’
9、If Write Result Indicator turn
- Green mean write success
- Red mead write fail
3
6
5
2
1
7
9
8
手机开机进META 模式
4

## Slide 20: How to debug when write fail

## Slide 21
1、How to debug when the operator fail? -- Actually all operator log information display on the main UI
2、If you want to get help from MTK, what information should I provide? -- As the No.1 refer , you can provide the UI Log and the META_DLL.log file, and the META_DLL.log file path default is “C:\”
-- If Smart Phone, SP_META_DLL.log also need.